## Slide 1: Drug Delivery

## Slide 2
Conventional
Controlled
Drug Delivery
Sustained
Extended
Site-specific
Pulsatile
Enteral
Parenteral
Other
In general medicine, enteral is feeding or drug administration by the digestion process of a gastrointestinal (GI) tract.
Parenteral is taken into the body or administered in a manner other than through the digestive tract, as by intravenous or intramuscular injection

## Slide 3: Oral Administration
Advantages
  Patient: Convenience, not invasive, higher compliance
  Manufacture: well established processes, available infrastructure
  After a drug is swallowed, it is absorbed by the digestive system and enters the hepatic portal system. It is carried through the portal vein into the liver before it reaches the rest of the body. The liver metabolizes many drugs, sometimes to such an extent that only a small amount of active drug emerges from the liver to the rest of the circulatory system. This first pass through the liver thus greatly reduces the bioavailability of the drug.
Disadvantages
  Unconscious patients cannot take dose
  Low solubility
  Low permeability
  Degradation by GI enzymes or flora
  First pass metabolism
  Food interactions
  Irregular absorption

## Slide 4: Oral Administration
Traditional oral delivery systems
  Tablets
  Capsules
  Soft gelatin capsules
  Suspensions

## Slide 5: Buccal/Sublingual
Advantages
  By-pass First pass metabolism
  Rapid absorption
  Low enzymatic activity
Disadvantages
  Discomfort during dissolution
  Probability of swallowing- lost of effect
  Small doses
Traditional delivery system/devices
  Tablets
  Chewing gum

## Slide 6: Intravenous (IV)
Advantages
  Drug 100% bioavailable
  Rapid response
  Total control of blood concentration
  Maximize incorporation of degradable drugs
  By-pass FPM
Disadvantages
  Invasive
  Trained personnel
  Possible toxicity due to incorrect dosing
  sterility
Traditional delivery system/devices
  Injection-bolus
  IV bag - infusion

## Slide 7: Subcutaneous
Advantages
  Patient self-administration
  Slow, complete absorption
  By-pass FPM
Disadvantages
  Invasive
  Irritation, inflammation
  Maximum dose volume - 2mL

## Slide 8: Inhalers

## Slide 9: Insulin Delivery Modes Syringes
Improved Technology:
disposable
thinner needles
more sanitary
Notes: 9

## Slide 10: Insulin Secretion

## Slide 11: Basal and bolus insulin concept
Basal insulin
  Suppresses glucose production between meals and overnight
  Nearly constant levels
  Upto 40 to 50% of daily needs
Bolus insulin (mealtime)
  Limits hyperglycemia after meals
  Immediate rise and sharp peak after 1 hour
  Approx 10 to 20% of daily requirement at each mealtime

## Slide 12: Insulin Delivery Modes Jet Injectors
sends insulin through the skin , using high pressure mechanism
an option for people with severe needle phobia

## Slide 13: Transdermal
Advantages
  Local effect
  Ease of administration
Disadvantages
  Low absorption for some drugs
  May cause allergic reactions
Requirements
  Low dosage <10 mg/mL
  MW< 1,000

## Slide 14: Limitations of Transdermal Delivery Systems
Skin structure poses a barrier on the mw of the drug (< 500 Da)
Usually reserved for drugs which are extremely potent (thus requiring a dosage of only a few mg).
  The largest daily dose of a drug from a patch is the nicotine patch, with delivers a daily dose of only 21 mg.

## Slide 15
Lidocaine
Product Name = Lidoderm®
Used for: analgesia of postherpetic neuralgia (PHN), a painful condition caused by the varicella zoster virus (herpes zoster = shingles)

## Slide 16: Iontophoretic Patches
Iontophoretic patches use a tiny electrical current to promote flow of the drug (usually charged) through the skin.

## Slide 17: Iontophoretic Patches

## Slide 18: Iontophoretic Patches
Lidocaine + Epinephrine
Product name = Lidosite
Used for: Dermal anesthesia
Type of Patch = Reservoir, iontophoretic.
Epinephrine acts as vasoconstrictor, thus prolonging the duration of action of lidocaine (by delaying resorption) at the site

## Slide 19: Microneedles Patches
Microneedles patches are currently being explored as mechanisms to deliver vaccines and larger macromolecules.

## Slide 28: Model Questions for Section III of 32 marks
Name 2 designs for artificial valves? (2 marks)
Name 2 products for HIV testing (1 mark)
PCR is used in which technology (1 marks)
Give 2 glucose sensing devices (2 marks)
Give 2 active and 2 passive drug delivery devices (2 marks)